## Slide 1
Inverse Algorithm Design
of Floor Plans
João David Inês Pereira Catarina Belém António Leitão

## Slide 2: Algorithmic Design

## Slide 3: Algorithmic Design
Automatic optimization
Parametric models
Steep learning curve
Costly
conversion

## Slide 4: Inverse Algorithmic Design
Algorithmic description
wall([p1, p2])
wall([p1, p4]
parts=[door(1, 0.7, rf),
window(2.3, 2)])
sink(xy(4.5, 7), 90)
Floor plan images
ML
algorithms

## Slide 5: Inverse Algorithmic Design
Model visualization
Floor plan images
ML
algorithms

## Slide 6: Inverse Algorithmic Design
Interpretation
Detect relevant symbols
Representation
Convert to a structured representation
Reconstruction
Create algorithmic description

## Slide 7: Inverse Algorithmic Design
Recognition
Segmentation
Vectorization
Input image
from CubiCasa5K

## Slide 8: Inverse Algorithmic Design
Recognition
Junctions
Walls and Railings
Symbols
Segmentation allows us to identify:

## Slide 9: Inverse Algorithmic Design
Recognition
Segmentation results :
Accuracy (%) | Rooms | Icons |  | 
 |  | Overall | Toilet | Sink
Our results | 82.5 | 97.5 | 98.9 | 98.5
CubiCasa5K | 82.7 | 97.6 | 72.5 | 67.4

## Slide 10: Inverse Algorithmic Design
Recognition
Vectorize structural elements
Recover semantics
We then use that information to:
Attach windows and doors to walls

## Slide 11: Inverse Algorithmic Design
Reconstruction
Define parameters
Write program
using Khepri
x1 = 1.41 y1 = 1.56
wall(p1, p2; parts=door(1, .5))
sink(xy(10, 15), 270)
...
Recognition
Segmentation
Vectorization
Input image

## Slide 12: Inverse Algorithmic Design
Reconstruction
Khepri as the chosen AD tool
Clustering to define certain values
Refactoring to improve readability and parametricity

## Slide 13: Inverse Algorithmic Design
Reconstruction
Define parameters
Write program
using Khepri
x1 = 1.41 y1 = 1.56
wall(p1, p2; parts=door(1, .5))
sink(xy(10, 15), 270)
...
Recognition
Segmentation
Vectorization
Input image

## Slide 14: Inverse Algorithmic Design
Reconstruction
Define parameters
Write program
using Khepri
x1 = 1.41 y1 = 1.56
wall(p1, p2; parts=door(1, .5))
sink(xy(10, 15), 270)
...
Recognition
Segmentation
Vectorization

## Slide 15: Examples

## Slide 16: Examples

## Slide 17: Examples

## Slide 18: Examples

## Slide 19: Examples

## Slide 20: Examples

## Slide 21: Reverse Algorithmic Design
Explores vectorial information
Two-step method
Extraction
Generates low-level program
Refactoring
Improves abstraction

## Slide 22: Reverse Algorithmic Design
polygon(xy(45, 7), xy(46, 7), xy(46, 6), xy(45, 6))
polygon(xy(51, 21), xy(51, 20), xy(50, 20), xy(50, 21))
polygon(xy(50, 14), xy(51, 14), xy(51, 13), xy(50, 13))
polygon(xy(50, 7), xy(51, 7), xy(51, 6), xy(50, 6))
polygon(xy(55, 7), xy(56, 7), xy(56, 6), xy(55, 6))
polygon(xy(60, 7.01), xy(61, 7), xy(61, 6), xy(60, 6))
polygon(xy(65, 21), xy(66, 21), xy(66, 20), xy(65, 20))
polygon(xy(65, 14), xy(66, 14), xy(66, 13), xy(65, 13))
polygon(xy(65, 7), xy(66, 7), xy(66, 6), xy(65, 6))
polygon(xy(70, 7), xy(71, 7), xy(71, 6), xy(70, 6))
polygon(xy(75, 21), xy(76, 21), xy(76, 20), xy(75, 20))
polygon(xy(75, 14), xy(76, 14), xy(76, 13), xy(75, 13))
polygon(xy(75, 7), xy(76, 7), xy(76, 6), xy(75, 6))
polygon(xy(80, 14), xy(81, 14), xy(81, 13), xy(80, 13))
polygon(xy(80, 7), xy(81, 7), xy(81, 6), xy(80, 6))
…

## Slide 23: Reverse Algorithmic Design
polygon(xy(45, 7), xy(46, 7), xy(46, 6), xy(45, 6))
polygon(xy(51, 21), xy(51, 20), xy(50, 20), xy(50, 21))
polygon(xy(50, 14), xy(51, 14), xy(51, 13), xy(50, 13))
polygon(xy(50, 7), xy(51, 7), xy(51, 6), xy(50, 6))
polygon(xy(55, 7), xy(56, 7), xy(56, 6), xy(55, 6))
polygon(xy(60, 7.01), xy(61, 7), xy(61, 6), xy(60, 6))
polygon(xy(65, 21), xy(66, 21), xy(66, 20), xy(65, 20))
polygon(xy(65, 14), xy(66, 14), xy(66, 13), xy(65, 13))
polygon(xy(65, 7), xy(66, 7), xy(66, 6), xy(65, 6))
polygon(xy(70, 7), xy(71, 7), xy(71, 6), xy(70, 6))
polygon(xy(75, 21), xy(76, 21), xy(76, 20), xy(75, 20))
polygon(xy(75, 14), xy(76, 14), xy(76, 13), xy(75, 13))
polygon(xy(75, 7), xy(76, 7), xy(76, 6), xy(75, 6))
polygon(xy(80, 14), xy(81, 14), xy(81, 13), xy(80, 13))
polygon(xy(80, 7), xy(81, 7), xy(81, 6), xy(80, 6))
…

## Slide 24: Reverse Algorithmic Design
p = xy(45, 6)
length = 1
for i ∈ 0:7
square(p+vx(5*i), length)
end

## Slide 25: Inverse Algorithmic Design
using KhepriAutoCAD
x1 = 0
x2 = 5 y1 = 0
y2 = 6
y3 = 8
# List of points created based on X and Y values.
p1 = xy(x1, y1)
p2 = xy(x1, y2)
p3 = xy(x1, y3)
# ...
# Definition of the walls based on the created points
thickwall([p1, p2])
thickwall([p1, p4]; parts=[door(1, 0.7, rf),window(2.3, 2)])
thinwall([p2, p5]; parts=[door(1, 0.7, lf)])
# ...
sink(xy(4.5, 7), π)
toilet(xy(2.5, 7.7), 3π/2)
closet(xy(4, 1), xy(5, 3))
show_auxiliary_labels(labels_only=true)

## Slide 26: Inverse Algorithmic Design
using KhepriAutoCAD
x1 = 0
x2 = 5 y1 = 0
y2 = 6
y3 = 8
# List of points created based on X and Y values.
p1 = xy(x1, y1)
p2 = xy(x1, y2)
p3 = xy(x1, y3)
# ...
# Definition of the walls based on the created points
thickwall([p1, p2])
thickwall([p1, p4]; parts=[door(1, 0.7, rf),window(2.3, 2)])
thinwall([p2, p5]; parts=[door(1, 0.7, lf)])
# ...
sink(xy(4.5, 7), π)
toilet(xy(2.5, 7.7), 3π/2)
closet(xy(4, 1), xy(5, 3))
show_auxiliary_labels(labels_only=true)

## Slide 27: Inverse Algorithmic Design
using KhepriRevit
x1 = 0
x2 = 5 y1 = 0
y2 = 6
y3 = 8
# List of points created based on X and Y values.
p1 = xy(x1, y1)
p2 = xy(x1, y2)
p3 = xy(x1, y3)
# ...
# Definition of the walls based on the created points
thickwall([p1, p2])
thickwall([p1, p4]; parts=[door(1, 0.7, rf),window(2.3, 2)])
thinwall([p2, p5]; parts=[door(1, 0.7, lf)])
# ...
sink(xy(4.5, 7), π)
toilet(xy(2.5, 7.7), 3π/2)
closet(xy(4, 1), xy(5, 3))
show_auxiliary_labels(labels_only=false)

## Slide 28: Inverse vs Reverse Algorithmic Design
Uses only raster images
Improves program readability
Adds semantics

## Slide 29: Conclusions
Generates parametric programs
Extracts relevant floor plan elements
Automatically creates an AD program

## Slide 30: Future Work
Using Bézier curves to approximate curve walls
Training with more data
Exploring vectorial information

## Slide 31
Thank You!
João David Inês Pereira Catarina Belém António Leitão