## Slide 1: Inverse Algorithmic Design
João Carlos Morgado David
Automatic Conversion of Floor Plan Images into Computer Programs

## Slide 2: Background
Technical drawings
Computer-Aided Design (CAD)
Building Information Modeling (BIM)

## Slide 3: Algorithmic Design
Algorithms are parametric
Parameters control variations
Steep learning curve
Costly conversion

## Slide 4: Inverse Algorithmic Design

## Slide 5: Inverse Algorithmic Design
Interpretation
Representation
Reconstruction
Detecting relevant symbols
Creating the algorithm
Converting to a structured representation

## Slide 6: Objectives
Parametric output
Intuitive floor plan description
Inverse Algorithmic Design

## Slide 7: Related Work

## Slide 8: Algorithmic Design
book_wall(p, fi, z) =
let (p1, p2, p3, p4, pa, pb) = (
p + vpol(mid_block_r() + library_door, fi),
p + vpol(mid_block_r() + block_l/2 + -(library_door/2), fi),
p + vpol(mid_block_r() + block_l/2 + library_door/2, fi),
p + vpol(mid_block_r() + block_l + -library_door, fi),
u0() + vx(-(wall_thickness/2)),
u0() + vxy(wall_thickness/2, block_h/4))
with(default_level_to_level_height, block_h/4) do
with(default_level, level(z)) do
wall([p1, p2])
wall([p3, p4])
end
end
end
torch_set(p, fi, z) =
let (p1, p2, p3, p4) = (
p + vz(man_h) + vpol(mid_block_r() + library_door, fi),
p + vz(man_h) + vpol(mid_block_r() + block_l/2 -library_door/2, fi),
p + vz(man_h) + vpol(mid_block_r() + block_l/2 + library_door/2, fi),
p + vz(man_h) + vpol(mid_block_r() + block_l + -library_door, fi))
(v2, v3) = (normal(p, p2, p2+vz(1), p+vz(1)),
normal(p, p3, p3+vz(1), p+vz(1)))
rotate(block_instance(astana_torch, loc_from_o_phi(add_z(p2, z), fi), 1),
-pi/8, p2+vz(z), v2)
rotate(block_instance(astana_torch, loc_from_o_phi(add_z(p3, z), fi), 1),
pi/8, p3+vz(z), v3)
end
KHEPRI

## Slide 9: Floor Plan Parsing — Before
Dosch et al., 2000 — A complete system for the analysis of architectural drawings
Constraint Network (Dosch et al., 2000)
Altered Hough Transform (Macé et al., 2010)
SURF & OCR (Ahmed et al., 2012)

## Slide 10: Floor Plan Parsing — Now
Liu et al., 2017 — Raster-to-Vector: revisiting floorplan transformation

## Slide 11: Floor Plan Parsing — Now
Lv et al., 2021 — Residential floor plan recognition and reconstruction

## Slide 12: Proposed Solution
Input image
Recognition
Reconstruction
Defining parameters
Program writing
Backend rendering
Symbols
Vectorization
Attaching wall elements
Semantics Recovery
using Khepri
x1 = 1.41
... y1 = 1.56
... wall(p1, p2; parts=door(1, .5))
sink(xy(10, 15), 270)
...
Walls & Junctions
Segmentation

## Slide 13: Segmentation
Input Image
Junctions
Walls and Railings
Symbols
Kalervo et al., 2019 — CubiCasa5K: A dataset and an Improved multi-task model for floorplan image analysis

## Slide 14: Segmentation Network
Kalervo et al., 2019 — CubiCasa5K: A dataset and an Improved multi-task model for floorplan image analysis

## Slide 15: Junction Heatmap Threshold

## Slide 16: Junction Heatmap Threshold

## Slide 17: Vectorization

## Slide 18: Wall Thickness Calculation
1
2

## Slide 19: Wall Thickness Calculation
1
2

## Slide 20: Choosing a Metric

## Slide 21: Choosing a Metric

## Slide 22: Semantics Recovery
Adapted from: Lv et al., 2021 — Residential floor plan recognition and reconstruction

## Slide 23: Example Image
Kalervo et al., 2019 — CubiCasa5K: A dataset and an improved multi-task model for floorplan image analysis

## Slide 24: Door Extraction
S
E

## Slide 25: Door Classification
S
E
O
Right
New example
Forward

## Slide 26: Other Examples

## Slide 27: Dataset Statistics

## Slide 28: Data Augmentation

## Slide 29: Toilets, Sinks, and Others
Kalervo et al., 2019 — CubiCasa5K: A dataset and an improved multi-task model for floorplan image analysis

## Slide 30: Toilets
Class: 0º

## Slide 31: Toilets
Class: 45º

## Slide 32: Toilets
Class: 180º

## Slide 33: Sinks
Class: 0º
Class: 0º (?)
Class: 315º (?)
CornerSink

## Slide 34: Integration
Liu et al., 2022 — A ConvNet for the 2020s

## Slide 35: Proposed Solution
Input image
Recognition
Reconstruction
Defining parameters
Program writing
Backend rendering
Symbols
Vectorization
Attaching wall elements
Semantics Recovery
using Khepri
x1 = 1.41
... y1 = 1.56
... wall(p1, p2; parts=door(1, .5))
sink(xy(10, 15), 270)
...
Walls & Junctions
Segmentation

## Slide 36: Defining Parameters

## Slide 37: Estimating Distances

## Slide 38
include("OutAux.jl")
delete_all_shapes()
thinwall(wallpath; parts=[]) = wall(wallpath, 0.15; parts=parts)
thickwall(wallpath; parts=[]) = wall(wallpath, 0.3; parts=parts)
# List of X and Y values. Alternatively, this part could be
# skipped and the points would use these values directly. x1 = 0
x2 = 5
y1 = 0
y2 = 6
y3 = 8
# List of points created based on X and Y values.
p1 = xy(x1, y1)
p2 = xy(x1, y2)
p3 = xy(x1, y3)
# ...
# Definition of the walls based on the created points
thickwall([p1, p2])
thickwall([p1, p4]; parts=[door(1, 0.7, rf), window(2.3, 2)])
thinwall([p2, p5]; parts=[door(1, 0.7, lf)])
# ...
sink(xy(4.5, 7), 90)
toilet(xy(2.5, 7.7), 180)
closet(xy(4, 1), xy(5, 3))
show_auxiliary_labels(labels_only=false)
Program Execution

## Slide 39
include("OutAux.jl")
delete_all_shapes()
thinwall(wallpath; parts=[]) = wall(wallpath, 0.15; parts=parts)
thickwall(wallpath; parts=[]) = wall(wallpath, 0.3; parts=parts)
# List of X and Y values. Alternatively, this part could be
# skipped and the points would use these values directly. x1 = 0
x2 = 5
y1 = 0
y2 = 6
y3 = 8
# List of points created based on X and Y values.
p1 = xy(x1, y1)
p2 = xy(x1, y2)
p3 = xy(x1, y3)
# ...
# Definition of the walls based on the created points
thickwall([p1, p2])
thickwall([p1, p4]; parts=[door(1, 0.7, rf), window(2.3, 2)])
thinwall([p2, p5]; parts=[door(1, 0.7, lf)])
# ...
sink(xy(4.5, 7), 90)
toilet(xy(2.5, 7.7), 180)
closet(xy(4, 1), xy(5, 3))
show_auxiliary_labels(labels_only=false)
Program Execution

## Slide 40
include("OutAux.jl")
delete_all_shapes()
thinwall(wallpath; parts=[]) = wall(wallpath, 0.15; parts=parts)
thickwall(wallpath; parts=[]) = wall(wallpath, 0.3; parts=parts)
# List of X and Y values. Alternatively, this part could be
# skipped and the points would use these values directly. x1 = 0
x2 = 5
y1 = 0
y2 = 6
y3 = 8
# List of points created based on X and Y values.
p1 = xy(x1, y1)
p2 = xy(x1, y2)
p3 = xy(x1, y3)
# ...
# Definition of the walls based on the created points
thickwall([p1, p2])
thickwall([p1, p4]; parts=[door(1, 0.7, rf), window(2.3, 2)])
thinwall([p2, p5]; parts=[door(1, 0.7, lf)])
# ...
sink(xy(4.5, 7), 90)
toilet(xy(2.5, 7.7), 180)
closet(xy(4, 1), xy(5, 3))
show_auxiliary_labels(labels_only=false)
Program Execution

## Slide 41
include("OutAux.jl")
delete_all_shapes()
thinwall(wallpath; parts=[]) = wall(wallpath, 0.15; parts=parts)
thickwall(wallpath; parts=[]) = wall(wallpath, 0.3; parts=parts)
# List of X and Y values. Alternatively, this part could be
# skipped and the points would use these values directly. x1 = 0
x2 = 5
y1 = 0
y2 = 6
y3 = 8
# List of points created based on X and Y values.
p1 = xy(x1, y1)
p2 = xy(x1, y2)
p3 = xy(x1, y3)
# ...
# Definition of the walls based on the created points
thickwall([p1, p2])
thickwall([p1, p4]; parts=[door(1, 0.7, rf), window(2.3, 2)])
thinwall([p2, p5]; parts=[door(1, 0.7, lf)])
# ...
sink(xy(4.5, 7), 90)
toilet(xy(2.5, 7.7), 180)
closet(xy(4, 1), xy(5, 3))
show_auxiliary_labels(labels_only=false)
Program Execution

## Slide 42
include("OutAux.jl")
delete_all_shapes()
thinwall(wallpath; parts=[]) = wall(wallpath, 0.15; parts=parts)
thickwall(wallpath; parts=[]) = wall(wallpath, 0.3; parts=parts)
# List of X and Y values. Alternatively, this part could be
# skipped and the points would use these values directly. x1 = 0
x2 = 5
y1 = 0
y2 = 6
y3 = 8
# List of points created based on X and Y values.
p1 = xy(x1, y1)
p2 = xy(x1, y2)
p3 = xy(x1, y3)
# ...
# Definition of the walls based on the created points
thickwall([p1, p2])
thickwall([p1, p4]; parts=[door(1, 0.7, rf), window(2.3, 2)])
thinwall([p2, p5]; parts=[door(1, 0.7, lf)])
# ...
sink(xy(4.5, 7), 90)
toilet(xy(2.5, 7.7), 180)
closet(xy(4, 1), xy(5, 3))
show_auxiliary_labels(labels_only=false)
Program Execution

## Slide 43: Results

## Slide 44: Segmentation Model
 | Rooms |  |  | Icons |  |  |  |  | 
 | Wall | Railing | Rest | Door | Window | Toilet | Sink | Closet | Rest
Acc (%) | 83.3 | 27.4 | 98.4 | 57.0 | 71.4 | 66.4 | 64.3 | 76.2 | 99.5
IoU (%) | 72.2 | 22.9 | 96.5 | 52.0 | 65.4 | 61.5 | 54.7 | 68.4 | 98.1

## Slide 45: Segmentation Model
 | Rooms |  |  | Icons |  |  |  |  | 
 | Wall | Railing | Rest | Door | Window | Toilet | Sink | Closet | Rest
Acc (%) | 83.3 | 27.4 | 98.4 | 57.0 | 71.4 | 66.4 | 64.3 | 76.2 | 99.5
IoU (%) | 72.2 | 22.9 | 96.5 | 52.0 | 65.4 | 61.5 | 54.7 | 68.4 | 98.1

## Slide 46: Segmentation Model
 | Rooms |  |  | Icons |  |  |  |  | 
 | Wall | Railing | Rest | Door | Window | Toilet | Sink | Closet | Rest
Acc (%) | 83.3 | 27.4 | 98.4 | 57.0 | 71.4 | 66.4 | 64.3 | 76.2 | 99.5
IoU (%) | 72.2 | 22.9 | 96.5 | 52.0 | 65.4 | 61.5 | 54.7 | 68.4 | 98.1

## Slide 47: Junction Detection
Class-agnostic detection
Class-dependent detection

## Slide 48
none
slide

## Slide 49: Orientation Classification
Toilets test set
Sinks test set
 | 0º-360º | Corner | Weighted Avg.
Recall (%) | 98.6 | 95.8 | 98.5
Precision (%) | 98.6 | 93.9 | 98.5
 | 0º-360º
Recall (%) | 98.9
Precision (%) | 98.9

## Slide 50: Example Results
Kalervo et al., 2019 — CubiCasa5K: A dataset and an improved multi-task model for floorplan image analysis

## Slide 51: Example Results

## Slide 52: Example Results

## Slide 53: Example Results

## Slide 55: Conclusions
Are hard to parameterize and optimize, which is a requirement nowadays.
Traditional design methods
Easy to iterate over but there is no easy conversion method, and it has a steep learning curve.
Algorithmic design
We automatically create AD programs from floor plan images:
New reconstruction method;
Semantic recovery process;
Output in the form of parametric AD programs.
Inverse algorithmic design
J. David and A. Leitão, “Getting a handle on floor plan analysis: door classification in floor plan images and a survey on existing datasets”, in Proceedings of the 10th International Conference of the Arab Society for Computation in Architecture, Art, and Design (2022): Hybrid Spaces of the Metaverse, Oct. 2022, pp. 22–235.
J. David, C. Belém, and A. Leitão, “Inverse algorithmic design: automatic conversion of floor plan images into computer programs”, in INTERCONNECTIONS: Co-computing beyond boundaries — Proceedings of the CAAD Futures conference, 2023, TU Delft Netherlands (submitted).
Contributions

## Slide 56: Conclusions
Are hard to parameterize and optimize, which is a requirement nowadays.
Traditional design methods
Easy to iterate over but there is no easy conversion method, and it has a steep learning curve.
Algorithmic design
We automatically create AD programs from floor plan images:
New reconstruction method;
Semantic recovery process;
Output in the form of parametric AD programs.
Inverse algorithmic design
J. David and A. Leitão, “Getting a handle on floor plan analysis: door classification in floor plan images and a survey on existing datasets”, in Proceedings of the 10th International Conference of the Arab Society for Computation in Architecture, Art, and Design (2022): Hybrid Spaces of the Metaverse, Oct. 2022, pp. 22–235.
J. David, C. Belém, and A. Leitão, “Inverse algorithmic design: automatic conversion of floor plan images into computer programs”, in INTERCONNECTIONS: Co-computing beyond boundaries — Proceedings of the CAAD Futures conference, 2023, TU Delft Netherlands (submitted).
Contributions
joaodavid@tecnico.ulisboa.pt

## Slide 57: Inverse Algorithmic Design
wall(xy(7.584039, 3.842963), xy(2.398200, 3.853195))
beam(xy(0.502686, 2.703664), xy(8.244835, 10.961915))
wall(xy(14.693588, 11.768203), xy(14.054853, 0.192584))
wall(xy(7.370911, 6.716919), xy(11.943345, 14.120184))
wall(xy(1.747752, 7.537068), xy(2.703668, 7.131730))
beam(xy(11.581883, 9.683602), xy(0.151352, 0.410725))
beam(xy(7.426873, 9.021476), xy(6.926079, 12.398898))
wall(xy(12.493763, 4.756162), xy(1.159009, 1.971081))
beam(xy(3.490791, 7.604907), xy(3.204002, 0.474994))
beam(xy(14.497536, 13.006465), xy(8.799677, 6.278438))
block(xy(10.517310, 9.367753))
block(xy(3.341927, 14.129803))
block(xy(5.478417, 8.914325))
block(xy(7.269629, 3.172376))
block(xy(13.184670, 13.796445))
block(xy(6.753180, 10.633837))
block(xy(1.574608, 0.533216))
block(xy(10.986766, 12.291348))
block(xy(13.317139, 1.794746))
block(xy(1.989959, 5.523614))
block(xy(3.171852, 8.748131))
beam(xy(4.102901, 7.008103), xy(0.064639, 5.828904))
beam(xy(0.379541, 5.330805), xy(11.256828, 2.661589))
wall(xy(2.084056, 13.388036), xy(13.611340, 9.179749))
beam(xy(3.847304, 3.357306), xy(0.132002, 10.896384))
wall(xy(1.692626, 11.254379), xy(10.204213, 1.378933))
wall(xy(10.563378, 10.510916), xy(8.537150, 11.153845))
beam(xy(2.467427, 11.791093), xy(10.066387, 6.674029))
wall(xy(10.481891, 1.151805), xy(1.071189, 8.043461))
beam(xy(6.657314, 7.561724), xy(1.523147, 0.549411))
beam(xy(8.167366, 12.537342), xy(3.505036, 2.041586))
KHEPRI

## Slide 58: Recovering Accurate Orientation

## Slide 59: Ellis, K., et al. (2018)

## Slide 60: Scale-Invariant Feature Transform (SIFT)
Lowe, 2004 - Distinctive Image Features from Scale-Invariant Keypoints

## Slide 61: Scale-Invariant Feature Transform (SIFT)

## Slide 62: Structural Symbol Recognition
Rezvanifar et al., 2019 - Symbol spotting for architectural drawings: state-of-the-art and new industry-driven developments

## Slide 63: Subgraph Isomorphism

## Slide 64: Constraint Network
Ah-Soon & Tombre, 2001 - Architectural symbol recognition using a network of constraints

## Slide 65: Convolutional Neural Networks
A Comprehensive Guide to Convolutional Neural Networks — the ELI5 Way (Towards Data Science)

## Slide 66: Attention and the Transformer
Dosovitskiy et al., 2021 - An image is worth 16x16 words: Transformers for image recognition at scale

## Slide 67: EfficientNetV2

## Slide 68: Graph Neural Networks
Song & Yu, 2021 - Framework for indoor elements classification via inductive learning on floor plan graphs

## Slide 69: Rotation Invariance
Objects can be detected in any orientation
Their rotation is discarded
Find image rotation and scale using automated feature matching (MathWorks)

## Slide 70: Floor Plan Parsing — Now
Zeng et al., 2019 — Deep floor plan recognition using a multi-task network with room-boundary-guided attention

## Slide 71: Floor Plan Parsing — Now
Zeng et al., 2019 — Deep floor plan recognition using a multi-task network with room-boundary-guided attention

## Slide 72: Floor Plan Parsing — Now
Zeng et al., 2019 — Deep floor plan recognition using a multi-task network with room-boundary-guided attention

## Slide 73: Residential Floor Plan Vectorization

## Slide 74: Avoid Placing Walls Over Junctions
1
2
3

## Slide 75: Avoid Placing Walls Over Junctions
1
2
3

## Slide 76: Used Loss Function

## Slide 77: CubiCasa5K Loss Function

## Slide 78: CubiCasa5K Loss Function

## Slide 79: CubiCasa5K Loss Function

## Slide 80: CubiCasa5K Loss Function

## Slide 81: Segmentation Network
 | Mean Room Type IoU (%) | Mean Icon IoU (%) | Heatmap MAE
Baseline (CubiCasa5K) | 60.72 | 55.73 | 0.00117
DFP-VGG-16 | 47.83 | 41.25 | 0.00141
DFP-ResNet34 | 47.88 | 38.36 | 0.00142
DFP-ResNet50 | 45.26 | 34.33 | 0.00147
DeepLabv3-ResNet50 | 58.72 | 57.25 | 0.00123

## Slide 82: Validation Loss Curves

## Slide 83: ConvNeXt Architecture

## Slide 84: EfficientNetV2

## Slide 85: ConvNeXt Architecture

## Slide 86: Door Description

## Slide 87: Why Extract Individual Images?

## Slide 88: Generating Parameters
p1 = (2.5, 8.0)
p2 = (2.6, 7.2)
p3 = (8.0, 7.3)

## Slide 89: Generating Parameters
p1 = (2.5, 8.0)
p2 = (2.6, 7.2)
p3 = (8.0, 7.3)
p1 = (1, 2)
p2 = (1, 1)
p3 = (2, 1)
Coordinate clustering
x1 = 2.55
x2 = 8.0
y1 = 7.25
y2 = 8.0
p1 = (x1, y1)
p2 = (x1, y2)
p3 = (x2, y1)
Generation

## Slide 90: Execution Time Analysis

## Slide 91: Failed Scale Estimation

## Slide 92: F-signatures
(Tabbone et al., 2003)

## Slide 93: Faster R-CNN
(Ren et al., 2017)

## Slide 94: Taking context into account
(Macé et al., 2010)